THINS
Sharp interface fluid vacuum flow
Vincent Moreau & Luca Massidda

---
SPH analysis
- The SPH model of a liquid metal target for the ESS has been analyzed as a test case. The model is a portion of the liquid metal bath, with rigid boundaries and a free surface.
- The code has run on a linux 64bit pc, the run time is approx 2 hours for 1 million particles and 0.1ms transient simulation.
- Energy, pressure and velocity magnitude distribution for half model are shown

---
SPH parallelization
- The limiting fctor for the previous simulation was on the model size due to the memory occupancy of the data structure.
- CUDA, OpenCL and FPGA technologies have been studied for an efficient porting of the code.
- The code has been redesigned with new data structures for parallelization.
- CUDA parallelization is almost complete.
- Simulations with 10million particles are foreseen for a single Tesla card.
- Speedup factor at the moment is almost 25x, the ESS simulation would take less than 5 minutes!
- Debugging and optimization phase has been started.